23 Peterson LLC

383 Dorchester Road

Lyme, NH 03768

381-2551 or 359-5039

Permit # 2012-33

Map/ID #  107/5

House renovations at

23 Peterson Road, Plainfield

06-01-12	Permit-2012-33, 23 Peterson Road. Discussed renovation of house with owner at the request of Steve prior to approving his permit. I let him know that I would need to see the plumber and electrician’s certification. I told him to call me when they start work as I want to see the house and go over some of the changes to the house. One of the bedrooms is going to be converted to a bathroom upstairs.

Time 0.2

09-05-12	Permit 2012-33, 23 Peterson Road. I stopped by as I haven’t heard from anyone and I was concerned they were too far along without notifying me. According to the contractor all the outside sheathing was replaced as well as the siding and the windows. In the two bedrooms one in the basement and one on the first floor have egress windows. All the walls are studded and they are getting ready to do the plumbing and electrical. I left my cards for them.

Time 0.4

03-22-13	Permit 2012-33, 23 Peterson Road. Call from owner to inspect the rough in electrical and plumbing so they could insulate. He had called me earlier last week to say that they would be ready next week. Everything was okay and I told them they could insulate. When they put new sheathing on the outside they furred out the studs to make them six inches instead of four.

Time 0.6

04-07-13	Permit 2012-33, 23 Peterson Road. I went by to inspect the insulation as they told me it would be done by now. I let myself in and inspected the insulation. They used six inches of cellulose blown in behind fabric. The ceiling insulation will be blown in once the sheetrock is installed.

Time 0.4

05-28-13	Permit 2012-33, 23 Peterson Road. I received a call to do a final inspection. When I got there they were still installing sheetrock. It will probably be a month before it is completed.

Time 0.3

David H Lersch

Plainfield Building Inspector