Robert & Hun Millard

16 Baynes Road

Meriden

510-0026

Permit # 2013-19

Map/Lot 105/22

28x44 2-story modular home with a car attached garage

25 Baynes Road

09-10-13	Permit 2013-19, 25 Baynes Road. I inspected the footer forms. Looks like for the garage but plans show garage and first floor of house on same level.  The rebar was installed and supported, bend at corners and a falls and tied. Ground wire installed. I gave the okay to pour concrete.

Time 0.7

09-13-13	Permit 2013-19, 25 Baynes Road. I inspected the wall forms and from the slope of the land and the lower wall forms (right end) are set up for a large opening for garage doors, it appears like the garage will be lower than the first floor. I will ask next time I am there. Wall forms looked okay. It is not a problem, but if that is the case it doesn’t match the prints.

Time 0.6

09-18-13	Permit 2013-19, 25 Baynes Road. I inspected the perimeter drains so they could backfill. I was there at the end of the day and they were gone. The drains stopped at the right end of the front and rear walls. The ground is high on the left side and slopes down to the right where the opening on the foundation is for garage doors. Blue foam was added to the walls and I could see the black sealant behind the foam along the top edge. The foam doesn’t go to the top of the wall and should unless they insulate the wall on the inside. I will have to call Robert and see what his plans are regarding the insulation and the house plans.

Time 0.6

09-24-13	Permit 2013-19, 25 Baynes Road. I went by to see what was going on and to get clarification about some issues. No one was there but the ground was excavated for a footer on the left side of the house for a garage.

Time 0.1

09-25-13	Permit 2013-19, 25 Baynes Road. Received a call from Dave to inspect the footer forms for the garage. The forms were okay and I looked at his print for the concrete work and it was different than the one I had. The prints with the permit were from New England Homes and the contractor had prints from Lavalley’s modular dated later. The right end that had an opening that looked as if for garage doors was for the walk out basement would be framed in. The square footage was also different. I need to call and get a correct set of prints.

Time 0.5

09-26-13	Permit 2013-19, 25 Baynes Road. I called owner but telephone number is out of service. Called contractor, left message. Contractor called and said New England Homes was brought out by Lavalley’s. He will drop off a set of prints Tuesday at the town hall.

Time 0.1

10-04-13	Permit 2013-19, 25 Baynes Road. Inspected the frost wall forms for the garage. Looked okay and told them they could order concrete.

Time 0.3

10-15-13	Permit 2013-19, 25 Baynes Road. Went by to see progress as I was out of town. The frost wall was poured and the ground was leveled out around the house and garage. The garage floor was prepared with sand so the floor could be poured.

Time 0.1

12-05-13	Permit 2013-25, 25 Baynes Road. Win performed the underground utility inspection. He said it was okay to cover.

Time 0.5

01-15-14	         Permit 2013-25, 25 Baynes Road. Hi Dave, The service for the PBS house being built on Baynes Rd. in Meriden is also

ready for Liberty U. to energize. Mt. Goat contracting is suppose to get me the seq.# later today, but I didn't know if you might be able to pass in the request without it.

1/14 Insp. of new service for new house on Baynes Rd. .75 hrs.

Win S

01-15-14	         Permit 2013-25, 25 Baynes Road. I notified Liberty U., okay to energize.

01-29-14	Permit 2013-25, 25 Baynes Road. (Win) Rough in elect. insp. of master bedroom over garage.

Time 0.75

02-19-14	Permit 2013-25, 25 Baynes Road. (Win)Final insp. at Baynes Rd. new house.

Time 0.5

02-20-14	Permit 2013-25, 25 Baynes Road.	(Win) Final insp. at Baynes Rd. new house. It's okay to give them a TCO at this time. There is still quite a bit of finish work to be completed inside and out. There is electrical work to be completed in the garage also, but it's essentially safe to be occupied at this time.

Time 0.75

03-26-14	Permit 2013-25, 25 Baynes Road. I called Pete to schedule a final inspection of the house. Win had inspected the house earlier and some items needed finished. The house was completed except the decks, etc. for the entrances and the master shower needed to be tiled and a door installed. They didn’t insulate the foundation except to grade. Pete has been requested to give them a quote to do the work and to seal the foundation better as the original contractor didn’t do it. I will issue a Certificate of Occupancy and a letter requesting that I inspect the decks and shower when completed.

Time 0.7

07-31-14	Permit 2013-25, 25 Baynes Road. Stopped by to see if any work was completed. Rear deck completed and front entrance.

Time 0.1

David H Lersch

Plainfield Building Inspector