Terry & Sandra Delisie

630 Kings Hwy WRJ, Vt

802-295-2036

Permit 2014-03

Map/Lot 225/15

replace mfg home with 26x52 modular

250 Willow Brook Road

04-14-14	Permit 2014-03, 250 Willow Brook Road. Met with the owner at the town hall to go over questions they had regarding the replacing their manufactured home with an modular home. They want to had a pedestal for the power so then can use the old home and when the new home is ready to disconnect the old one and connect power to the new one. We also talked about when and what needed to be inspected and also the IECC requirements.

Time 1.1

05-01-14	Permit 2014-03, 250 Willow Brook Road. Met with Jeremy toinspect the footer forms and answered questions about slab insulation. The contractor wasn’t going to put in rebar when I talked to Jeremy by telephone on Tuesday. I told him it needed two rows, supported, and tied together. Forms were okay. I asked the contractor if he was going to put vertical rebar in and he said no. I told him he needed them installed and every  four feet. Owner agreed to cost increase. They are trying to find out ways to meet code for the IECC slab insulation. They are going to put two inches of blue board four feet deep along the frost wall on the inside. Since the basement slab is going to be poured over the top of the frost wall, he is going to put the four by two-inch piece of blue board on the outside edge of the frost wall and pour the floor up to the blue board. It is not exactly to code but will provide some frost protection.

Time 1.0

Received telephone calls from Champion Builders who are building the modular home about wind speed since the codebook doesn’t specify for our area. After searching last night, I found Lebanon uses 90mph and to the east of is 90mph as well as NY once you are away from the Connecticut River valley. If I couldn’t give them a letter, they would be forced to use 110mph. I emailed him a letter stating that the base wind speed was 90mph. This figure would be adjusted upward using IRC2009 chart for wind modification for topographical wind effect.

Time 0.3

05-04-14	Permit 2014-03, 250 Willow Brook Road. I inspected the side-wall and rear wall forms and the frost wall forms for walk out basement, looked okay.

Time 0.9

05-07-14	Permit 2014-03, 250 Willow Brook Road. Inspected the perimeter drains along the front of the house so they could backfill.

Time 0.6

05-09-14	Permit 2014-03, 250 Willow Brook Road. Inspected the rest of the perimeter drain, foundation sealing, R10 blue foam along the inside of the frost wall for the walk out basement. Also the sewage drain pipes for the basement future bathroom. Looked okay.

Time 0.7

05-21-14	Permit 2014-03, 250 Willow Brook Road. Went to inspect the trench for the buried electrical to the new house. The conduit was down three feet as I requested and he installed three two inch conduits. The conduit to the old house was four inch and part of it was uncovered. Lots of water down by the pole and the conduit wasn’t sticking straight up the pole and he said when the water goes away he will get it straight as mud too soupy to hold it now.

Time 0.5

06-01-14	Permit 2014-03, 250 Willow Brook Road. Inspected the meter panel and connection to the electrical panel on the first floor of the modular home.

The meter is on the front left of the house and the panel is upstairs in the laundry at the rear of the house. Looked okay and did a walk through the modular home. Still needs some siding put on and inside where the two halves came together.

Time 0.9

06-18-14	Permit 2014-03, 250 Willow Brook Road. Terry asked me to inspect his modular home and if I could issue a temporary Certificate of Occupancy as he needs to move into the new home before they can take the old manufactured home and there are several items that can’t be completed until the old home is gone. Items are: Front deck and stairs for the front door; water hooked up from well to pressure tank (using hose between old and new); temporary hook up to septic as new pipe needs to be put in after old home is moved and allowing access to tank and leach field. Other items that need to be completed is the basement insulation that is currently being installed. The front door will be secured with screws so it cannot be opened until the deck is built. House is completed except for the above items. Still needs some landscaping work but he will wait until the old house is gone. I will issue a ninety day temporary CO.

Time 0.9

David H Lersch

Plainfield Building Inspector