Patricia Aiken (Trustee)

PO Box 117

Cornish Flat, NH 03746

469-3815

Permit # 2016-67

Permit # 2017-71

Map/Lot 224/11

renovate portions of house and add a 24x32 addition

258 Ladieu Road

09-26-16	Permit 2016-67, 258 Ladieu Road. I met with Brian to go over plans for the house. The kitchen area will stay the same but the bedrooms, bathrooms, and pantry will be changed. The hall will reconstructed in the new 24x32 addition which will house the two bedrooms that were in the old house.

Time 0.8

10-11-16	Permit 2016-67, 258 Ladieu Road. Dave called to have me inspect the floating slab for the addition of the two car garage. Looked okay. Also discussed the addition to the house as all the excavation was completed. He will be doing the footer and will call when he is ready for inspection. They will be using foam block construction for the wall which will give an R23 value for insulation.

Time 0.5

10-12-16	Permit 2016-67, 258 Ladieu Road. Dave called to have me inspect the footer forms with rebar and ground wire installed. Okay to pour.

Time 0.4

10-20-16	Permit 2016-67, 258 Ladieu Road. Dave called and said the foundation foam blocks were in place with rebar. Also drilled holes in foundation to install rebar to connect addition foundation wall to house foundation.

Time 0.7

03-28-17	Permit 2016-67, 258 Ladieu Road. Met with Dan Michaud 558-4005 and inspected the framing that has been completed. We went over project and he will call if any questions and will let me know when he is ready for any inspections. A new service entrance panel installed with Kohler generator and transfer switch. Old panel is still being used and new wiring will be installed to new panel and old panel removed.

Time 0.7

05-23-17	Permit 2016-67, 258 Ladieu Road. Charlie called to have me inspect the rough in electrical wiring and to go over plans to insulate some of the new addition's basement. I also inspected some of the new wiring (replacing all electrical wiring) and some of the rough in plumbing. Discussed the chimney flues that supported wood stoves that will not be used. I told him to seal off the one upstairs with cement as it is the same flue as the downstairs wood stove that will be replaced with a propane stove.

Time 1.4

06-05-17	Permit 2016-67, 258 Ladieu Road. Had an appointment to inspect the 			rough in electrical. Was late getting there, no one there, scheduled for next 		day.

Time 0.5

06-06-17	Permit 2016-67, 258 Ladieu Road. Met with Johnny, the electrician, 			inspected the new panels, most all of the old circuits have been replaced. 			Looked okay and said they could insulate..

Time 0.8

10-23-17	Permit 2017-71, 258 Ladieu Road. Was supposed to meet Charlie on 			Saturday but forgot, stopped by to see progress. Attic insulated by blown 			in and foam hoods around LED canned lights. Headers were sprayed foam 		as well as the walls. Sheetrock installed, siding being installed, and 			flooring installed. Contractor said it probably will be spring when 				everything is finished. Charlie may want to move in before everything was 		finished and I told them the requirements for a Temporary CO.

Time 0.6

11-10-17	Permit 2017-71, 258 Ladieu Road. Dropped off the Oil Fired Permit and 			inspected the boiler, one zone connected, needs relief valve piped to four 			inches from floor. All the main floors were finished, radiant heated tile 			floor in the kitchen. Getting close to where I could issue a temporary 			Occupancy Permit.

Time 0.6

02-01-18	Permit 2017-17 258 Ladieu Road. I met with Charlie on-site at 258 Ladieu 		2/1(?). He walked me through the home. The upper level appears complete 		or at the final paint stage with the exception of a section of wall to the left 			of the door by the entry where there is a wire protruding from a wall 			opening (weather station feed). On the lower level the grid is installed for 			a dropped ceiling and rough-in feeds are run for lights in the grid, but no 			enclosures. There are no smokes on the lower level and I suggested that he 		talk to you about locations, but that there should probably be at least two 			on that level (1 in boiler area, 1 in living space) Upstairs there are 				detectors in each bedroom, but I didn’t see one in the hall outside the 			bedrooms. I indicated that I thought there should be one in the hall, but I 			deferred to you. The gas range (400lbs) is in place, but Charlie said that 			there is a shut-off at the floor level, at the transition from the flex supply to 		copper gas line that drops into the basement and then outside to regulator 			and tank. (Do we or Bill Taylor do anything to check these installations?) 			Charlie indicated that he is waiting for the electrician to return to wore the 			lights in the suspended ceiling and that he was happy to install smoke/co 			detectors and that he would contact you to plan that work. He is anxious to 		move in before roads get messy and was asking about a C.O.  given that 			the upper level is complete and he doesn’t know when the electrician will 			be able to return. I deferred to you.

In thinking about that visit, I’m remembering that there were some 				penetrations in the boiler room electrical and radiant tubing that were not 			fire-stopped. If you are talking to Charlie you might mention it to him. I 			assume I will be returning for the final “Final”, but it will be easier if he 			takes care of it before the drop ceiling tiles are installed. I can call him 			directly if you want.

02-02-18	Permit 2017-71, 258 Ladieu Road. Talked to Brad about his inspection. 			Called Charlie to let him know that he should have two smoke detectors in 		the basement and one outside bedrooms. He was sure there was one in the 			hall, would check, drop ceiling in basement and let him know what 			hardware was needed to mount detectors to grids. He will tell electrician.

Time 0.1

02-15-18	Permit 2017-71, 258 Ladieu Road. Talked with electrician and Brad. 			Checked codes and let electrician know a CO was required outside 				bedrooms and smoke detectors in bedrooms and outside bedrooms. There 			is a CO detector outside mechanical room and he will install two smoke 			detectors in the basement when the drop ceiling is installed.

Time 0.2

02-21-18	Permit 2017-71, 258 Ladieu Road –Monday / Wednesday - Charlie Aiken: 		Met electrician (Jeremy Cramer) on-site for “final” interior. 3rd Smoke 			installed as requested. Remaining outlets/switches plated and lights in 			suspended ceiling connected. The only remaining electrical items inside 			are the weather station and range hood fan. Both are waiting on exterior 			carpentry work (siding/trim) which is in progress.

02-25-18	Permit 2017-71, 258 Ladieu Road. Received Brad's report and I will issue

the Certificate of Completion.

David H Lersch

Plainfield Building Inspector