Michael Malone

PO Box 191

675-2301

Permit # 2011-63

Map/Lot 256/26

24x40 garage with second floor

26 Sugar Hill Road

04-12-12	Permit 2011-63, 26 Sugar Hill. I received a call to inspect the trench from the meter pedestal to the barn. This is the first time at the site and the building walls and roof were constructed. There was quite a lot of ledge and the frost wall was deep enough for the rear wall and less around the rest due to ledge. The trench and conduit were ready to backfill and the panels were mounted in the building and on the pedestal. I told him the trench would need six inches of sand due to the ledge and rocky soil.  I gave the okay to backfill. He was thinking of radiant heat in the slab and I told him to call if he did prior to pouring concrete.

Time 0.9

07-30-12	Permit 2011-63, 26 Sugar Hill Road. I inspected the floor with the radiant pipes installed and pressure tested, wire mesh on pedestals, floor is ready to pour. The electrical service is completed from the house to a disconnect on a pedestal and then in buried conduit to the meter panel with a disconnect and mounted on a pedestal near the utility pole. The conduit needs to be installed to the pole and PSNH will pull the wires from the pole to the meter panel.

Time 0.6

09-04-12	Permit 2011-63, 26 Sugar Hill Road. Michael called to have me inspect some of the rough in wiring and plumbing as well as the insulation he was installing downstairs and upstairs. The upstairs will be finished later, he just wants to insulate it in for the winter. I also notified PSNH that everything was okay to connect power to the meter panel.

Time 0.7

David H Lersch

Plainfield Building Inspector