Elizabeth A. Greene

268 Willow Brook Road

469-3640

Permit 2013-28

Map/Lot 224/22

replace 10x28 deck

08-23-13	Permit 2013-28, 268 Willow Brook Road. I inspected the framing for the new deck with contractor. Maximum height is 30 inches. Main deck is around one foot high. There are two sets of steps to both rear entrances that the individual steps are comprised of three platforms that are stacked on top of each other getting smaller in area. He will be putting some kind of railing for the steps.

Time 0.8

01-13-14	Permit 2013-28, 268 Willow Brook Road. (Win) I also went today to 268 Willow Brook Road to do a final insp. of the deck. The contractor was there, but there were no railings installed at either door location. I told him that to receive a full CO for the permit that I felt you'd need to have those railings installed. It didn't seem like the CO was a condition for him to receive is final payment. He said he'd tell the homeowner of the necessity of having the railings installed to get a CO for the project.

David H Lersch

Plainfield Building Inspector