Robbie Williams

281 Route 12A

469-3954

Permit # 2018-11

Map/Lot 203/21

36x50 garage

05-02-18	Permit 2018-11, 281 Route 12A. Dave called and said the slab forms were ready for inspection, inspected forms with two rows of rebar, wire mesh. Looked okay, let him know he could pour.

Time 0.4

07-07-18	Permit 2018-11, 281 Route 12A. Robbie called to have me inspect the aerial electric service entrance on his garage. Inside panel and meter panel okay as well as entrance cable from peak to meter. I will notify Liberty Utilities it is okay to connect service.

Time 0.4

10-26-18	Permit 2018-11, 281 Route 12A. Inspected garage, wall plates off as he just finished painting walls. Everything looked okay except he had a hot forced oil furnace and I let him know that he needs to call Bill Taylor and fill out the State oil burning permit. Once that is completed and signed off by Bill, I will issue the completion certificate.

Time 0.5

04-18-19	Permit 2018-11, 281 Route 12A. I received the signed oil burning permit by the Fire Chief and issued the Certificate of Completion.

David H Lersch

Plainfield Building Inspector