Lundy's Property Maintenance LLC

316 Route 120

Plainfield, NH 03781

448-5120

Permit #2017-69

Map/Lot 226/10.1

40x60 Butler Steel Building

09-26-17	Permit 2017-69, 316 Route 120. Was supposed to inspect footer forms around 1PM, on way back from Croydon Road, stopped by. Footer forms were almost ready for inspection. Rebar installed, tied and supported, vertical L rebar tied to horizontal rebar, ground wire installed. They just needed a few pieces of rebar where the steel framing beams needed to rest. I told them to go ahead when ready.

Time 0.2

09-29-17	Permit 2017-69, 316 Route 120. Haven't heard from Barden Concrete and I was going past so I stopped by. Wall forms were up and concrete was poured. Bank inspector was there and he wasn't happy either. I told him I would call Barden and let them know they should have called. In the phone message I told them that if they ever poured again without contacting me they would have to tear down and start again. There was no excuse for them going ahead without any notification to the bank or me.

Time 0.3

10-10-17	Permit 2017-69, 316 Route 120. Inspected the trench from the building towards the road with sand on the bottom and the conduit installed. Not sure where Liberty will put the pole so it will end temporary. They used schedule 80 conduit as vehicles will be driving over that area.

Time 0.2

10-23-17	Permit 2017-69, 316 Route 120. Inspected the floor insulation, rebar supported on bricks and radiant heat plumbing for the concrete slab floor.

Looked okay.

Time 0.4

11-02-17	Permit 2017-69, 316 Route 120. Barden Concrete called to have me inspect the slab forms in front of two garage doors. Rebar set on bricks, tied together, and 5-6 inches in depth. Okay to pour.

Time 0.5

David H Lersch

Plainfield Building Inspector