Troy Hall

374 Route 12A

Plainfield

298-7209

Permit # 2016-41

Map/Lot 218/9

30x44 steel building

08-30-16	Permit 2016-41, 374 Route 12A. Inspected the forms for the footer for the 30'x44' building with rebar supported and ground wire installed. Looked okay and told them they could pour.

Time 0.3

09-06-2016	Permit 2016-41, 374 Route 12A. Inspected the frost wall and the three inches of blue wall insulation.

Time 0.4

09-30-16	Permit 2016-41, 374 Route 12A. I inspected the blue foam sheets of insulation on the sand fill before the floor was poured. All okay.

Time 0.4

10-04-16	Permit 2016-41, 374 Route 12A. Troy was assembling the wall and roof steel framing. Base plates will be anchored to slab.

Time 0.3

Troy Hall – 374 Route 12-A               New Construction: Utility Building

Date: Dec 7, 2016       Permit #:2016-41         Activity: Inspect for overhead service.

Met with owner on-site. Meter box mounted on NE corner of gable end. Ground wire present. Mast / weather head attached w/ single guide wire above roof. Owner plans to spray insulation on walls / ceiling leaving 2” +/- of steel framing exposed for mounting electrical conduit for interior fit-out.

15 min. Brad

12-06-16	Permit 2016-41, 374 Route 12A. Looked at pictures Troy sent for 				electrical service. Notified Brad by email and phone to inspect. Notified 			Liberty Utilities it was okay to connect service by email.

05-09-17	Permit 2016-41, 374 Route 12A. I did the final inspection of the 30x44 steel building used for storing bee keeping equipment and processing honey. Looked okay and I will issue a Certificate of Completion.

Time 0.5

David H Lersch

Plainfield Building Inspector