Jason C Downs

427 Center of Town Road

675-2314

Permit # 2012-49

Permit # 2013-44

Permit # 2014-64

Permit # 2015-41

Permit 2016-62

Map/ID # 242/2

40x32 Two story SFH with basement

07-12-12	No Permit, Center of Town Road. I had an appointment with Jason to go over his plans to build a new house further back on the property and his current house will be his workshop (currently as his house). We discussed requirements and inspections for egress windows, buried utilities, insulation, and etc. He had a full set of plans from Lavalleys including the truss design.

Time 1.8

08-14-12	Permit 2012-49, 427 Center of Town Road. Dave called to have me inspect the footer forms for the house. Looked okay.

Time 0.5

08-28-12	Permit 2012-49, 427 Center of Town Road. Jason called to have me inspect the perimeter drains so he cold backfill. I was surprised to find out the walls were poured and I wasn’t called by Dave. Jason said that Dave installed all the rebar he designed and had pictures. I told him he could backfill.

Time 0.7

09-22-12	Permit 2012-49, 427 Center of Town Road. Jason called to have an inspection of the drains in the basement prior to pouring the floor. I inspected the plumbing and the first floor joists/beams. He is putting radiant heat in the basement slab. He will call when all the heat pipes are installed as well as the blue foam insulation under the pipes. The plumbing for the basement bathroom has the sewage pump installed in the floor as his septic system will be at a higher elevation. He also installed radon pipes that he will cap in the basement to be used if ever needed in the future.

Time 1.0

11-08-12	Permit 2012-49, 427 Center of Town Road. I met with Jason to go over his plans for the manifold for his radiant heat and the clearances for the vent for the wall mounted boiler and distance from a possible location of a wood stove where the chimney will be located. There will not be any windows above the boiler vent and I told him to make sure the vent is not in the corner of the foundation wall and where the chimney will be. Other than the heating that will be installed this year, the rest will wait until spring. He has started to dig the trench for the power and he is not sure it will ready before next year. He will provide temporary power on an 15 ampere circuit from the house for the boiler.

Time .08

06-30-15	Permit 2014-64, 427 Center of Town Road. Inspected the trench with conduit and cables installed from the pole to the concrete pull box down near the end of the driveway for the new house. Looked okay. Also Bruce was there from NH Co-Op. They want me back at three o'clock to inspect the trench, conduit and cables as well as the pedestal with the meter panel with the disconnect.

Time 0.8

06-30-15	Permit 2014-64, 427 Center of Town Road. Inspected the  trench, conduit and cables as well as the pedestal with the meter panel with the disconnect.

Time 0.5

06-30-15	Permit 2014-64, 427 Center of Town Road. Inspected the trench with conduit and cables installed from the pole to the concrete pull box down near the end of the driveway for the new house. Looked okay. Also Bruce was there from NH Co-Op. They want me back at three o'clock to inspect the trench, conduit and cables as well as the pedestal with the meter panel with the disconnect.

Time 0.8

06-30-15	Permit 2014-64, 427 Center of Town Road. Inspected the  trench, conduit and cables as well as the pedestal with the meter panel with the disconnect.

Time 0.5

07-01-16	Permit 2016-41, 427 Center of Town Road. Met with Jason to do some rough in inspections. We discussed his plans and that it would be a while before it would be completed as they are paying as they go.

Time 1.2

09-15-16	Permit 2016-62, 427 Center of Town Road. I inspected the rough in electrical and the rough plumbing that will be hidden by the installation of the insulation. Looked good except he needed to fire stop holes between floors where plumbing and wires go through.

Time 0.9

09-26-16	Permit 2016-62, 427 Center of Town Road. Inspected the installation of the insulation and verified holes fire stopped.

Time 0.9

04-25-19	Permit 2016-62, 427 Center of Town Road.	Jason called the other day to have me inspect his house so he could get an occupancy permit. Scheduled for today. Needs steps to right entrance, porch on front door, decks on rear of house for first floor patio doors and one for second floor door in bedroom. Radiant heat installed and working, water heater working, no flooring installed (hardwood flooring ready to be installed on first and second floor. Attic all finished except for hand railing on stairs and railing for the edge of the floor where the stairs are. Bathroom floors, ceramic installed, downstairs bathroom no fixtures, upstairs bathrooms, one has shower and toilet and no vanity installed, other bathroom just flooring installed. Walls are being painted and most electrical boxes need wall plates installed. Basement and main stairs need handrails and main stairs are open on one side, no railing. Main stairs are temporary, open between treads. Basement is insulated, vapor barrier installed, no sheetrock yet. Area for bathroom has plumbing, interior walls do not have sheetrock yet. Wires in electrical boxes have wire nuts installed, no devices and no cover. Kitchen area has electrical and plumbing, but no installed kitchen. I told Jason to get a temporary CO he would need a working kitchen, one completed bathroom, all wall plates installed and either devices with wall plates or blank wall plates installed, railing for stairs, and banisters installed in attic, second floor next to hole for stairs and along one side of main stairs. I also let him know his permit expired in August 2017 and a letter was sent at that time, never got a response.

Time 1.2

David H Lersch

Plainfield Building Inspector