Raymond Becker Jr.

44 Hopkins Road

802-299-6443

Permit # 2016-16

Map/Lot 264/9

26'8x48 Manufactured Home

05-12-16	Permit 2016-16, 44 Hopkins Road. Inspected the pedestal and utility pole for the electrical service. Saw pictures of the trench as the service is buried. Okay and notified Liberty Utilities.

Time 0.9

06-06-16	Permit 2016-16, 44 Hopkins Road. Inspected the slab for the house and looked at the pictures they took of the rebar that was installed. Way more than required an all was supported by chairs. Good job.

Time 0.6

06-16-16	Permit 2016-16, 44 Hopkins Road. I went by as units were to be set on slab. Only one half was there.

Time 0.5

06-20-16	Permit 2016-16, 44 Hopkins Road. Both units placed and assembled. No tie downs yet or utilities.

Time 0.6

06-21-16	Permit 2016-16, 44 Hopkins Road. Tie downs installed.

Time 0.3

06-29-16	Permit 2016-16, 44 Hopkins Road. I inspected the plumbing  under the home that connects the septic to the home and  the electrical connections as well. A small deck was built on the gable end for the front door and was not attached to the home and was resting on concrete pads. The state should inspect the septic today, so the only thing left is to build the deck on the lower side of the home and install the skirting.

Time 0.3

David H Lersch

Plainfield Building Inspector