Lisa Guaraldi

462 Willow Brook Road

496-3670

Permit # 2017-87

Map/Lot 215/15

Temp. HUD mobile home 6 months max

11-24-17	Permit 2017-xx, 462 Willow Brook Road. The house was getting new shingles and the membrane that was on the roof came off during the storm we had with lots of wind and rain. The roof is just boards with gaps between and the water soaked the insulation, flooring, etc. Inspected the temporary electrical hook up to the mobile home. Some of the ceilings exposed and sheetrock and insulation was removed. Some electrical fixtures had water pouring out of them during the storm. The electrical wiring looked okay, no damage that I could see, but wasn't a very neat install and probably some of it was added later. The house is set up as two living spaces with the kitchen area divided into two kitchens. The insurance adjuster has been out and is coming back as they found more areas that have damage, also mildew is forming on underside of roof boards. Liz wondered about the wiring and I told her they could replace switches, lights, outlets without having to update to current code, but if they start rewiring , then it would have to meet code. She would like to have a separate electric service for the apartment. I suggested since the main panel is in a shed in the back yard and is buried to house to two sub panels that the apartment could have aerial service from the pole to its own meter and main panel. That would involve rewiring the whole house.

They will call when the sewage and water lines are connected.

Time 1.5

12-05-17	Permit 2017-87, 462 Willow Brook Road. Phone call from Liz stating the temporary home has the water and sewage hooked up. I will have Brad go by to inspect.

Time 0.2

12-05-17	Permit 2017-87, 462 Willow Brook Road – Gurauldi (sp?) Met owner on site 					reviewed temporary hook-up for elect, water, and sewer. Lines appeared properly 					install and protected.

05-23-18	Permit 2017-87, 462 Willow Brook Road,. Mobile Home Removed, Permit closed.

David H Lersch

Plainfield Building Inspector