Liz Guaraldi

462 Willow Brook Road

496-3670 cell

Permit # 2018-01 for house repair and arena

Map/ID #215/5

11-24-17	Permit 2018-01, 462 Willow Brook Road. The house was getting new shingles and the membrane that was on the roof came off during the storm we had with lots of wind and rain. The roof is just boards with gaps between and the water soaked the insulation, flooring, etc. Inspected the temporary electrical hook up to the mobile home. Some of the ceilings exposed and sheetrock and insulation was removed. Some electrical fixtures had water pouring out of them during the storm. The electrical wiring looked okay, no damage that I could see, but wasn't a very neat install and probably some of it was added later. The house is set up as two living spaces with the kitchen area divided into two kitchens. The insurance adjuster has been out and is coming back as they found more areas that have damage, also mildew is forming on underside of roof boards. Liz wondered about the wiring and I told her they could replace switches, lights, outlets without having to update to current code, but if they start rewiring , then it would have to meet code. She would like to have a separate electric service for the apartment. I suggested since the main panel is in a shed in the back yard and is buried to house to two sub panels that the apartment could have aerial service from the pole to its own meter and main panel. That would involve rewiring the whole house.

They will call when the sewage and water lines are connected.

Time 1.5

12-28-17	Permit 2018-01, 462 Willow Brook Road. Liz called and said she was applying for a permit. She is using Bernie Hutchkins and will be having spray foam insulation and some interior work but no electrical.

Time 0.2

02-23-18	Permit 2018-01, 462 Willow Brook Road – Horse Farm (Guaraldi). 			Wednesday / Friday – Met Bernie Huckins on-site for upper level 				Electrical / Plumbing rough-in prior to insulation/sheetrocking. 				Upstairs/downstairs interior completely (minor exceptions) gutted to 			framing with some new interior partitions for Duplex (pre-existing use? 			Permitted?). New framing in exterior walls upstairs for new egress 				windows and new door to planned deck. Bernie indicated that he planned 			to use lags to attach deck. (Do you ask for mnfr lit on hardware to ensure 			size, quantity, pattern selection meets code?) Existing floor joists attached 			to center carrier with hangars. Hangars attached w/various fastener types, 			including some roofing nails. I mentioned it to Bernie. Maybe they should 			add some fasteners? They have sprayed insulation on the underside of the 			roof  and exterior walls (upper level only so far) (What should be the 			required thickness)? New upstairs plumbing connects to existing work in 			lower level. DWV pressure test observed on both units (one each visit). 			Upper level electrical also ok (Bernie seems to plate everything in a 2x4 			wall). Apparently there were 2 services? I believe Bernie indicated that 			they were eliminating 1 service. There is a new load center in the 				“apartment” which I understand will be a sub-panel for the new single 			service entrance in the lower level. Smokes in each bedroom.  There was a 		gas fireplace operating on my second visit – not sure if this was temp heat 			or permanent. Does Bill Taylor inspect this? How does he get notified?

03-16-18	Permit 2018-01, 462 Willow Brook Road.

Thank you Lisa for calling this morning and Ray for meeting with me 	yesterday at the site on Willow Brook road. Since we met I have spoken 	with our Primary Building Inspector, Dave Lersch, and Town 	Administrator Steve Halleran regarding the steel building. As we 	discussed the Town would like to see the stamped drawings for the steel 	building and a stamped drawing for the foundation design. A copy of the 	plot plan that locates the new building on the property would also be 	appreciated (I believe Ray indicated that this exists, or is easily done?). 		Dave and I will look into what else, if anything, will be required. This will 	be based on how you intend to use the building, so Lisa, if you can 	forward that description to us we will go from there.

Ray, from the inspection perspective, you can continue to erect the 	building with the understanding the no insulation or other interior covering 	finishes are planned. If that changes just call for electrical inspection 	before anything is covered up. If any electrical will be underground we 	will want to see the trenching/rough-in, before backfill. Dave will 	coordinate any inspections and he can be reached at: 603-381-1929. I am 	available as back-up at 603-675-2815.

If either of you have any questions please call Dave or I.

04-04-18	Permit 2018-01, 462 Willow Brook Road. Met with Bernie and inspected 	the new wiring, plumbing, upstairs almost finished, need kitchen 	countertops and some bath fixtures. Downstairs is all framed and some 	wiring 	is installed. Removing old electric heaters and installing baseboard 	radiators, there is a new boiler being installed. Five-eights sheetrock 	installed on both sides of wall separating the two living areas.			Time 0.5

06-05-18	Permit 2018-01, 462 Willow Brook Road. Lisa called and wanted me to 			inspect the building as she had several concerns. I inspected the steel 			building that had the roof panels on as well as the two sides. A fairly large 			number of panels had extra holes when the screws missed the structure 			and were taken out. I could not see the roof panels but several screws were 		missing on the side panels. Some of the panels had damage. Several of the 			horizontal framing members were sagging and a couple had some damage. 		I told Lisa that she should request and damaged panels and ones with 			holes in them be replaced as well as any damaged framing. Roof panel 			overhang was not consistent, especially on the back side.  I noticed that all 		the cables were not installed. Overall work was not very professional 			done. The two large door frames on the gable ends not supported as piers 			were used instead of a frost wall and were being supported by a piece of 			lumber jammed under a short piece of horizontal framing to the top of the 			pier. Lisa wondered about the open space between the bottom of the walls 			and the ground there is one to two foot gap that would have not been there 			if a frost wall was used.

Time 1.5

04-12-18	Permit 2018-01, 462 Willow Brook Road. Inspected the plumbing and 	electrical wiring rough in for the basement under the main part of the 	house. Five-eights fire code sheetrock will be installed to separate the two 	halves of the duplex including the ceiling. They also installed all new 	windows upstairs with egress in the bedrooms. New windows will be 	installed in the basement or lower level with egress in any bedrooms. All 	the wiring was replaced at the request of the insurance company and 	egress windows for the bedrooms. She decided to replace all the windows. 	Time 0.9

05-23-18	Permit 2018-01, 462 Willow Brook Road. Bernie called to have a final 	inspection on the left upstairs apartment. He installed 5/8 fire code 	sheetrock on all walls and in the attic to separate units. Apartment looked 	okay. I also inspected the rest of the house. The right side upper apartment 	is almost completed. The downstairs apartment will be for Liz under most 	of the house. Walls and ceiling will be 5/8 sheetrock. A small apartment in 	the left section of the basement containing a bath, bedroom, and one other 	room, may be used for caretaker. It has its own outside entrance. 	Bathroom may be used for the users of riding arena. Liz will be requesting 	a permit for two decks on rear of house, 8 feet high for the two 	apartments. Left apartment sliding doors will have board screwed to 	secure doors until deck completed.

Time 0.7

06-15-18	Permit 2018-01, 462 Willow Brook Road. After talking with Brad I 	downloaded the steel building instructions. from what I read all the 	temporary cables were supposed to be on the building until all the panels 	were installed. This was not what I observed when I was there before. 	Only one or two of the permanent  cables were installed. The directions 	also stated that if the directions were not followed the warranty may be 		voided.

Time 0.5

09-28-18	Permit 2018-01, 462 Willow Brook Road. I stopped in to check on 	progress. Horse barn the same as when I was last there except trim for 	large doors on each end were installed. The house has all the new siding 	installed, two new rear decks built, no stairs, just sliding doors for access. 	All outside receptacles installed. Inside almost finished, all new windows 	installed with egress ones for the bedrooms.

Time 0.3

10-31-18	Permit 2018-01, 462 Willow Brook Road. Bernie and I did the final walk 	through of the three apartment house. The left upstairs apartment was 	inspected earlier and now the left downstairs two room apartment with 	bathroom with entrance out the rear of the house was inspected. The right 	side apartment has a lower lever and the main floor. I did not find any 	issues, all walls and ceilings were 5/8 sheetrock. All new electrical and 	some plumbing was installed. House completely resided with vinyl siding 	and the two new decks accessed from sliding doors from the main level. A 	complete new propane heating system was installed. I will issue a 	completion certificate.

Time 0.5

04-22-19	Permit 2018-01, 462 Willow Brook Road. Met with insurance adjusters, 	Liz, steel building representatives, etc. to answer any questions they had. I 	gave them the copy of the few inspections for the barn and said Liz had 	copies of drawings, emails, etc.

Time 1.2

David H Lersch

Plainfield Building Inspector