Roland and Wanda Daniels

50 RjKris Lane, WRJ

802-299-7673

Permit # 2014-26

Map/Lot 102/11.2

Ranch modular and garage

52 Bonner Road

07-01-14	Permit 2014-26, 52 Bonner Road. Inspected the footer forms for the house. Okay.

Time 0.6

07-02-14	Permit 2014-26, 52 Bonner Road. When driving back from Marsh Lane, I went by 54 Bonner Road site. Some of the wall forms were up and the contractor said it would be ready for inspection on Tuesday. I will go around 7AM to inspect.

Time 0.3

07-07-14	Permit 2014-26, 52 Bonner Road. I inspected the forms for the slab for the Lavalley’s detached garage. Okay to pour.

Time 0.3

07-08-14	Permit 2014-26, 52 Bonner Road. Inspected the wall forms for the foundation. It was okay and told they could pour.

Time 0.3

07-29-14	Permit 2014-26, 52 Bonner Road. Stopped by to inspect the work. Pink 2 inch foam outside foundation. Let him know that it should be 3 inches. They will add one inch on the inside. Foam needs to be installed along the walk out basement side of the house from the floor down 4’. The rear wall will be insulated on the inside to r-19.

Time 0.2

08-07-14	Permit 2014-26, 52 Bonner Road. Inspected the two car detached garage that was completed and did a walk through the modular house as it was just set this week.

Time 0.4

08-19-14	Permit 2014-26, 52 Bonner Road. Stopped by to see the progress on the house. They are still installing the floors. The basement steps are installed.

Time 0.5

09-18-14	Permit 2014-26, 52 Bonner Road. Inspected the rough in electrical in the basement as well as the plumbing. Basement walls framed to meet R20 code for insulation. Okay to insulate.

Time 0.4

David H Lersch

Plainfield Building Inspector