Andrew Martin

520 Willow Brook Road

4

Permit # 2017-80

Map/Lot 215/10

530 Willow Brook Road

Modular home from Dales with mud room to attached garage

12-4-17	Permit 2017-80, 530 Willow Brook Road. Scanned reports, permit papers I had for this permit and emailed to Brad.

Time 0.3

12-05-17	Permit 2017-80, 530 Willow Brook Road. Phone call with Dale and Brad about footer forms that Brad inspected. Mud room between house and garage will have a basement (root cellar) house and garage will have a slab with a footer and frost wall.

Time 02.

- 12-05-17	Permit 2017-80, 530 Willow Brook Road – Dales – Foundation footing. Met 				concrete sub on-site. “Root cellar footing @80% complete formed. Exposed ledge 			in footing required a step in the footing. Formwork was not the most impressive, 				but adequate. Sub indicated that horizontal rebar would be raised with cmu brick 				and pictures taken to verify.

- 12-07-17	Permit 2017-80, 530 Willow Brook Road – Dales – Foundation wall – Stopped by 			– no-one onsite, Foundation walls partially assembled some rebar in place, more 				nearby. Noticed that wall forms not centered on footing in a couple of places (at 				the edge in 2 places) Subsequent trip - met concrete sub on-site. Sub described 				remaining work, including horizontal rebar and extra rebar around 3’x3’ opening 				for future access to crawlspace. 3rd trip: walls forms complete, braced. Blanketed 				due to anticipated snowfall.

12-07-17	Permit 2017-80, 530 Willow Brook Road. Dale called to have the wall forms inspected for the mud room.

Time 0.1

Brad went by and the outside panels were up and rebar installed. Text to Dale as I didn't get pictures of forms.

12-08-17	Permit 2017-80, 530 Willow Brook Road. received pictures of forms and gave the okay to pour.

Time 0.1

12-20-17	Permit 2017-80, 530 Willow Brook Road. Left word for Brad that the house footer forms were ready. I told Dale that if Brad didn't get there, send me pictures, I will review and if okay I will send a text that okay to pour. Talked to electrician about ground wire, he said NH-Co-Op still wanted the ground. Sent a email to NH Co-Op requesting clarification.

Time 0.3

12-26-17	Permit 2017-80, 530 Willow Brook Road. Received pictures of frost wall forms for the house, reviewed and gave the okay to pour.

Time 0.1

01-08-18		Permit 2017-80, 530 Willow Brook Road. I talked to Dale last night.

The house is a double wide manufactured home not a modular. He

will send pictures of frost wall perimeter drains. They are going to

pour slab for house, has a drain in the center to the perimeter drain to

get rid of any water under the home that might occur. Going to use

plywood and vinyl siding instead of skirting and attaching Roxul

insulation. Under the slab he will install vapor barrier. In the root

cellar the floor will be gravel with a vapor barrier and instead of blue

foam he will use Roxul as it is fire resistant so he won't have to cover.

Above will be a breezeway and not heated. There will be a access

from the root cellar to the crawl space. Home will be on concrete

blocks and will be anchored.

Time 0.3

01-15-18		Permit 2017-80, 530 Willow Brook Road. Dale called about setting

the house. Normally the frames are supported on single 8" concrete

blocks, two high. This house will be on columns made up of four, 8

inch concrete blocks. He wanted to know if he needed to do two

columns instead of one. I told him that because of the height and

possible stability issues, to use double columns. Dale agreed.

time 0.1

01-25--18	Permit 2017-80, 530 Willow Brook Road. Received a text about the

footer forms stating they wanted to pour garage footer Monday. Sent

pictures and looked okay. Brad went by on Friday and the footer was

poured and they were putting up the frost wall forms.

Time 0.2

01-29-18	Permit 2017-80, 530 Willow Brook Road. Received text and pictures of garage frost wall. Looked okay and let them know it was okay to pour.

Time 0.2

03-11-18		Permit 2017-80, 530 Willow Brook Road. Hi Dave,

I met w/Dale on Saturday. There were 3 items to fix before owner

moves in (all dealing w/steps @ entry doors) which he said would be

taken care of today. Does Bill Taylor inspect combustion devices in

manufactured housing or are they assumed to be inspected

already? Told Brad it is covered by the manufacturer.

03-15-18	Permit 2017-80, 530 Willow Brook Road. I’ll be stopping by Dale’s 	project on willow brook road later today to confirm that the steps have 		been addressed. Any word from Bart on when they plan to pour? Any 	other activity I should have on my radar?

Brad

03-16-18	Permit 2017-80, 530 Willow Brook Road. Brad said steps were okay and 	after the ground is landscaped the bottom temporary step will be removed. 	Still have half of the garage roof to finish.

03-19-18	Permit 2017-80, 530 Willow Brook Road. Talked to Dale and garage roof	is finished so I will issue a Certificate of Occupancy and email to Town 	Hall.

Time 1.0

03-22-18	Permit 2017-80, 530 Willow Brook Road. Dale’s Homes. I called the 			electrician regarding an electrical rough-in inspection for the breezeway 			and I agreed that I would stop by Friday 3/23 ~8:30am. I arrived as 			planned. The work looked fine except that the penetrations in the wall 			plates needed to be sealed. I spoke with a laborer to find out who’s job it 			would be, and when they planned to cover-up. The laborer did not know. I 		later received a call from the electrician. We agreed that he would take 			care of the holes and send you pictures. I asked the electrician if he knew 			when they were planning to insulate / sheetrock and he indicated that he 			was about to speak w/Dale and would forward my question. I spoke with 			Dale a few minutes later and he understood that we would want to see the 			insulation before sheetrock. His (carpenter? Sub-contractor?) called me 			later and agreed to call you when the insulation was done, probably early 			this week. I spoke with you to ask the question about R values required, 			given that the space, although new construction and insulated, was not 			going to have a heat source.

03-27-18	Permit 2017-80, 530 Willow Brook Road. Electrician called about rough-

in for the breezeway. I will schedule Brad. I thought house was finished

as last I heard the garage roof needed the roofing finished and Dale told

me it was all done.

time 0.1

03-28-18	Permit 2017-80, 530 Willow Brook Road. Elliott Brown, electrician called

and hasn't heard from Brad.

Time 0.1

03-29-18	Permit 2017-80, 530 Willow Brook Road. Phone call with Brad and 	contractor. Brad got with Elliott and will inspect the rough-in. Also talked

to contractor as Brad had him call me about insulation in the breezeway.

It is not conditioned space, but told him to use R-19 in walls and only r-38

in ceiling.

Time 0.2

04-04-18	Permit 2017-80, 530 Willow Brook Road. Received a call to inspect the

insulation in the breezeway and garage. Looked okay. The wall adjoining

the mud room will have sheetrock to the roof sheathing at my request. I

also walked through the house and signed the form on the meter panel.

The garage floor hasn't been poured yet.

Time 0.5

David H Lersch

Plainfield Building Inspector