Melissa Robb

P.O. Box 318

650-8734

Permit # 2013-58

Map/Lot 102/11.1

28x44 ranch modular home w/walkout basement

54 Bonner Road

01-23-14	Permit 2013-58, 54 Bonner Road. (Win) I went and did an inspection of the footings at the house being built on Bonner Road today. They had the rebar done properly and made provision for the ground from the rebar in the footing. They were also to cover the poured footing with thermal blankets to protect the curing cement from freezing. They'll be pouring the walls in the next few days and are going to supply me with photos, as I won't be able to get there before the walls are poured. I will be inspecting the footing drains and exterior foundation waterproofing/insulation prior to the foundation being back filled with sand after curing for 7-10 days after the walls are poured.

David H Lersch

Plainfield Building Inspector

I got your message that you're back in town!! You made it before the next snow event that's coming this week!
I had planned on going to the meeting tonight, but am experiencing some back pain and really aren't up to going out tonight, in fact I my not venture out tomorrow unless I can get some relief over the next few hours.
I did get your message earlier about 54 Bonner Rd(?) and the seq.# 267319904 (?) being too long. The best remedy would be for you to speak directly with the electrician ( Erik) and his # is 603-667-7781 ( hopefully that's a right # ).
He was to have guyed the mast to the roof, added a clamp/clip to the ridged pipe itself and installed an Intersystem Bonding terminal by the meter for grounding the phone or cable systems.
One other note about this new house...The general contractor never contacted me to do an inspection on the insulation/ sealing of the foundation or to see the foundation drainage system prior to the excavation contractor backfilling the foundation. 
We'll have to get together sometime soon for coffee...once this winter weather let's go!!
Glad you made it back safely!!! My job with the city is about to become full time again. I just turned 62 and will be going back to work full time...doesn't make much sense...but I'll take it!
Take care, Win Spencer Jr.

03-07-14	Permit 2013-58, 54 Bonner Road. email from Win regarding the electrical service hook up. They should be ready on Monday and I will notify Liberty. Wrong work order, emailed Win and he would have the electrician call me with the correct work order number.

03-10-14	Permit 2013-58, 54 Bonner Road. I went by to inspect the service entrance to see if the ground connections were made and that the mast had the support wire installed as mentioned in Win’s email earlier. Looked okay and with the correct work order number, I notified Liberty they could connect.

Time 0.4

03-19-14	Permit 2013-58, 54 Bonner Road. Met with Josh to see the progress as the owner is hoping to move in soon. The electrical service is not connected yet as well as the water and sewer. They cut the insulation at grade and Josh has reinstalled most of it and the rest when the ground thaws. So far it looks okay and will go back when utilities are connected.

Time 0.7

04-11-14	Permit 2013-58, 54 Bonner Road. I met with Josh to do the final inspection of the new modular home. Because the ground was still frozen some items weren’t finished, as well as the rear foundation wall wasn’t insulated yet. I will issue a CO with an attached letter stating that they have 90 days to build the front entrance steps/porch, rear deck, insulate the

interior rear basement wall (walk out basement), grade around the house for proper drainage, and close in the left overhang. Josh said the overhang will be completed before she moves in as well as the basement wall insulation. The grading, deck and entrances will be completed after mud season. There are temporary steps for the side entrance.

Time 0.7

07-31-14	Permit 2013-58, 54 Bonner Road. Went by to see progress. Blue insulation installed on left front corner, left overhang completed, grading completed. The side and front entrances need permanent steps and the rear deck needs built.

Time 0.1

09-08-16	Permit 2013-58, 54 Bonner Road. Dropped by today as I thought I saw a rear deck. The deck was all completed and will file this report.

Time 0.4