Chris & Amanda Jewell

PO Box 414

Meriden

381-9897

Permit # 2013-61

Map/Lot 252/92

40x28 modular two story cape

65 Whitaker Road

11-13-13	Permit 2013-61, 65 Whitaker Road. I was told that the footer forms would be ready on Tuesday, but contractor called and said because of ledge it wouldn’t be ready until this morning. It wasn’t started yet and made plans to inspect it tomorrow morning around 10AM.

Time 0.5

11-14-13	Permit 2013-61, 65 Whitaker Road. I got there around 10:30AM and they were still working on the forms, rebar laid in the forms and bent around corners and down the two falls (changes in elevation of footer). I told them about the ground wire and they weren’t informed and would call their boss and get the wire. Also they were not going to use chairs and suspend the rebar and I told them it needed to be supported and tied together. I would come back after the KUA meeting and they said they should be ready.

Time 0.4

11-14-13	Permit 2013-31, 65 Whitaker Road. The forms were almost ready, ground wire installed, I told them they could pour.

Time 0.5

11-18-13	Permit 2013-31, 65 Whitaker Road. The wall forms were up with rebar except for a few inside panels. They looked okay. Let them know they could order concrete.

Time 0.4

11-19-13	Permit 2013-31, 65 Whitaker Road. Went to inspect the footer forms for the garage. Due to ledge removal they weren’t ready, so I told them I would be back as I needed to be in Meriden at 2:30 anyway.

Time 0.7

11-19-13	Permit 2013-31, 65 Whitaker Road. Went by on my way to KUA to see if the footer forms were ready. They were with rebar installed and supported.

Time 0.4

11-20-13	Permit 2013-31, 65 Whitaker Road. Inspected the frost wall forms for the garage. I told them they could pour.

Time 0.3

02-21-14	Permit 2013-31, 65 Whitaker Road. (Win) Electrical service insp. at 65 Whitaker Rd.

Time 0.5.

02-25-14	Permit 2013-31, 65 Whitaker Road. Email from Win regarding electric service hook up. Notified Liberty Electric okay to connect.

Contractor will call when trench is ready to inspect. From the transformer to the house.

Time 0.2

David H Lersch

Plainfield Building Inspector