Constance McCoy

674 Willow Brook Road

254-5024

Permit # 2017-76

Map/Lot 215/4

renovation

10-11-17	Permit 2017-76, 674 Willow Brook Road. Going by noticed car there, Michelle said someone was doing work there, stopped and talked to owner. Walls were bare and she said they would be doing some electrical, new front door, side entrance new porch roof, steps. Said made deck smaller. She will get a permit.

Time 0.3

10-17-17	Permit 2017-76, 674 Willow Brook Road. Contractor called and wanted my to come by and go over some things. We covered insulation requirements and some solutions to make 2x4 walls meet energy code, windows for the bedrooms to meet egress code, and fire stopping electrical and plumbing holes. He will be adding a few outlets and may remove some.

Time 0.7

03-26-18	Permit  2017-76 674 Willow brook road (red& yellow house)  (Leslie?) 			Partial Electrical rough-in (ground floor, exterior walls, street side, gable 			end, kitchen. Owner is doing the electrical work. Everything looked ok. 			He has installed a row of exterior facing outlets along the street side eave 			wall. He indicated that they would be GFCI protected and have rated 			covers. (Is there a rated cover/receptacle that works on a standard wall 			box?) He indicated that the sink location was not changing and that the 			venting would be though the roof via a new 2x6 interior wall that was 			framed, but the plumbing was not roughed in yet. I believe he said the new 		range would have an exterior venting hood, but it was not cut in yet. He 			had furred out the walls as you requested for insulation including solid 			wood (dbl 2x6?) headers over the windows, but there appeared to be only 			~1” for insulation on the interior face of the headers. I suggested that he 			might consider rigid for those spots, but that I would talk to you about 			what was required.

08-24-18	Permit 2017-76. 674 Willow Brook Road. Met with contractor and 				inspected the insulation in the ceiling, It was a cathedral ceiling but only 			had R-30 due to rafters and should be R-38. The walls were furred out to 			make room for R-19 insulation. Several areas need additional receptacles, 			he needs some three feet from corners and any wall greater than two feet 			should have them as well. Brad inspected downstairs in the front half and 			it has sheetrock installed. Told him to check there as well as furniture in 			the way. All the wiring is new and let him know that he needed arc fault 			breakers. He is going to replace the panel and due a buried service 				entrance. Advised him I needed to see trench and conduit. . He is going to 			build decks on the left side of the house, two at first floor and one without 			stairs from the second floor bedroom with sliding doors. I told him to go 			down four feet and since one of the decks will be a screened porch, I 			suggested to use big foot forms at the bottom of the piers.

Time 0.5

09-27-18	Permit 2017-76, 374 Willow Brook Road. Received a call to come over 			when I was at 462 WBR. I inspected the rough in electrical and plumbing 			for the two bathrooms and the additional receptacles I requested on earlier 			inspection. Insulation installed and I let him know that he could continue 			installing sheetrock on the second floor. All windows in two bedrooms 			upstairs had egress windows installed.

Time 0.3

03-28-19	Permit 2017-76, 374 Willow Brook Road. Wanted to sheetrock ceiling, 			took pictures of can light wires so he could cover.

Time 0.1

03-18-19	Permit 2017-76, 674 Brook Road. Leslie rough-in (partial). Met 				Leslie on site. Only wanted to consider bedroom on northwest 				corner of the house (rough-in for sheetrock). Requested that he re-				set / increase fiberglass insulation in band joist (ceiling) and foam 				cracks between framing in rim area. Everything else looked ok. 				Gave him the ok to cover-up after insulation fixed.

David H Lersch

Plainfield Building Inspector