7 Bean Road Assoc, LLC

123 Gleason Road

PO Box 423 Meriden

Thomas Lappin

469-3004

Permit # 2012-25

Map/Lot 104/4

3rd floor kitchenette apartment at 7 Bean Road

05-07-12	Permit 2012-25, 7 Bean Road. Tom called for me to inspect the rough in electrical and plumbing for the third floor kitchenette apartment. Looked okay and looked at ways for a second egress. He will probably divide the large hallway on the second to accommodate both a hall and an egress hall to the stairs to the first floor. He needs to check to see if he needs a sprinkler system for the apartments if he uses the first floor commercially.

Time 1.2

10-02-12	Permit 2012-25, 7 Bean Road. Tom divided the second floor hall lengthwise to create a separate hall for a second egress for the third floor apartment. There is a fire rated door from each second floor apartment to the hall that leads to the stairs to the first floor. He needs to have the one apartment’s door swing inward so as not to block the stairs. Tha trhirde floor apartment looked okay and all egress halls were 5/8” fire code sheetrock. He needs to put a fire rated door at the top of the stairs from the first floor and at the bottom of the stairs on the second floor that goes to the third floor. At the bottom of the third floor stairs he needs to build a platform on the second floor side of the door. I will issue a Temporary Certificate of Occupancy so he can use the apartment until these things are completed.

Time 08.

10-04-13	Permit 2012-25, 7 Bean Road. Tom called to have me go over some codes for the restaurant regarding egress, exit and emergency lighting.

Time 0.6

David H Lersch

Plainfield Building Inspector