Dennis A Allen

82 William Gage Road

448-0548

Permit # 2011-46

Map/Lot 211/2

28x36 garage

09-08-11	Permit 2011-46, 82 William Gage Road. I inspected the floating concrete slab forms with rebar installed for the garage. Everything was okay to pour. Dennis and I discussed his plans for aerial electrical service to his garage and construction plans.

Time 1.0

11-12-11	Permit 2011-46, 82 William Gage Road. Dennis called and said the trench with the conduit laid will be ready early afternoon and wanted me to inspect it so he could backfill the trench. Looked okay as well as the post and beam construction of the garage.

Time 1.0

David H Lersch

Plainfield Building Inspector