Scott Krueger

830 Route 12A

558-4000

Permit # 2016-06

Permit # 2017-04

Map/Lot 237/02

Residence on second floor of shop building

02-18-16	Permit 2016-06, 830 Route 12A. I met with Scott to go over his plans for the partial second floor of his shop. We covered plumbing, electrical, insulation and egress concerns. He will be putting in about five windows and a door on the backside of the shop with a metal landing with steps for emergency exit. He will call when he gets some framing completed as well as electrical and plumbing. Plans sound good and I told him to call if he had any questions.

Time 0.7

08-24-16	Permit 2016-06, 830 Route 12A. Johanna called to have me do a electrical rough in inspection of 1/2 of the apartment. All the walls were studded and she was using metal clad electrical cable (MC). An egress door was installed on the rear for the future deck and stairs. Egress windows installed in the three bedrooms. Looked good.

Time 0.5

09-25-17	Permit 2017-04, 830 Route 12A. Inspected the plumbing and the one working bathroom, laundry  and the kitchen, rough in plumbing for the other bathrooms. Smoke detectors installed, most electrical fixtures installed, temporary light fixtures in several areas. saw pictures of the rough in and verified with pictures and sight the fire stopping of all penetrations to the floor below.

Time 0.6

09-25-18	Permit 2017-04, 830 Main Street. Letter sent on 04-22-18, no response as of this date. Permit expired, no CO or CC.

David H Lersch

Plainfield Building Inspector