Johannes Swarts

PO Box 36

709-7121

Permit # 2015-23

Map/Lot 105/12

renovate kitchen

86 Bonner Road

06-23-15	Permit 2015-23, 86 Bonner Road. Picked up Brad at Garfield's and went 			to inspect the work on the kitchen renovation. One area had a wall taken 			out to make a large bedroom. The outside wall needed receptacles 				installed to meet distance code. Also the kitchen had two circuits and will 			be GFI. The floors are sagging and Brad showed me where he is going to 			put a beam and posts as the floor joists are 2x8 and that is not large 			enough for the span. In other areas he is going to put the beams on the 			concrete block walls that are there already. Cabinets should be coming in 			about a week.

Time 0.8

David H Lersch

Plainfield Building Inspector