469-3136

Permit #2008-

Map/Lot

    - Permit – applied for. Telephone call from owner about moving his mobile

home and doing an addition to it as well as questions regarding codes for buried electrical service. It will be going under part of the driveway and should be schedule 80 and 18 inches deep. Where the conduit goes over a culvert pipe it will have to have 2-4 inches of concrete over it as it will be less that a foot. 469-3136, cell 359-2536

Time 0.3

10-16-08	Permit XXXX, Got a call again about the moving of a mobile home to his land and about a wood stove and electrical questions. Had a call from him back in June. I told him he needed a permit for the wood stove and it had to be inspected by the Fire Chief. Also he should get the book for it or information from the manufacturer as clearances are different by stove. I also mentioned about vent pipe and the different ones and each had different clearances. As to his electrical question if he can’t get to 18 inches for the conduit he needs to have 4 inches of concrete above it and extend to at least 6 inches to each side. He is working with NH Co-Op to get a pole set, etc.

Time 0.8

David H Lersch

Plainfield Building Inspector