Christian Forman

PO Box 64

Meriden

359-0997

Permit #2018-19

Map/Lot 101/2

185 Main Street

Barn and equipment shed

05-24-18	Permit 2018-19, 185 Main Street. Received a call as I was going to 	Connecticut that they wanted a footer inspection. I told him I couldn't do it 	till tomorrow and he needs to give me more that one or two hours 	notification for inspections. He said he could send pictures. I told him my 	requirements about rebar, ground wire and he said no problem. I told him 	once I received the pictures and reviewed them I would text okay to pour. 	I told him not to pour until he hears from me. Too late to try for Brad.

Time 0.2

05-31-18	Permit 2018-19, 185 Main Street. Went down the street as I was at the 	town hall to see if they were getting ready to pour the wall. Wall was 	poured last night and they were taking off the forms. I sent a text to Jim, 	contractor as to why he poured without inspection. He left me a phone 	message that he thought once I gave they okay for the footer, he didn't 	need to call again. I left him a phone message and told all concrete pours 	need to be inspected. He only had permission to pour the footer.

Time 0.4

05-31-18	Permit 2018-19, 185 Main Street. Sent text to Jim Mason about frost wall 			being poured without inspection. He called me later in the day and said his

foremen said I told him I didn't need to see wall with rebar installed as he 			worked on the Edgewater farm's building. I let Jim know I did inspect the 			wall forms with rebar twice on November 1st. He asked what he 				could do, I said not much since it was already poured. I will just note 			inspection report to say "no frost wall inspection".

Time 0.2

06-05-18	Permit 2018-19, 185 Main Street. Inspected the PEX plumbing that will 			supply water to hydrants in both sections of barn. Hydrants installed in 			insulated tubes. Looked okay.

Time 0.5

07-11-18	Permit 2018-19, 185 Main Street. I inspected the wire mesh, grounds 			wires grounding the mesh and metal pipes for the milking area and the 	plumbing drains for the milking area so they could pour the concrete floor. looked 	okay.

Time 0.8

08-08-18	Permit 2018-19, 185 Main Street.

Hi Dave,

I inspected work at Forman Barn. Everything looked fine. I told them I would report to

you and you would confirm that they are ok to sheetrock that center section around the

stairs.

Brad

Forman Main Street  8/8

09-14-18	Permit 2018-19, 185 Main Street. Inspected main panel, lighting, 				receptacles and electrical circuits. All railings, etc. installed, just need two 			large garage doors. All barn style doors installed.

Time 0.3

10-04-18	Permit 2018-19, 185 Main Street. Inspected completed barn. Landscaping 			completed, all doors installed. Waiting on utility company to set pole so 			wires can be connected to utility. All work electrical work is completed 			inside, just need power to meter panel. I will issue a Certificate of 				Completion and if an inspection is needed for NH Co-Op, I can go by and 			inspect power hook up.

Time 0.5

10-10-18	Permit 2018-19, 185 Main Street. Inspected electrical service from pole to 			meter panel on end of barn. Notified Liberty Utilities. WO#301838-01025.

Time 0.4

David H Lersch

Plainfield Building Inspector