Kimball Union Academy

PO Box 188

Meriden

469-2152

Permit # 2019-03

Map/Lot 103/1

Full Renovate

13 Chellis Road

02-22-19	Permit 2019-03, KUA 13 Chellis Road.

Headmasters House Renovation partial rough-in inspection for 			insulation.

Met E&G lead, Mike Pushee, on-site. First visit. Walked through 			entire building to understand scope. Specifically reviewed rough-in 			electrical / plumbing in exterior walls. Extensive structural re-work 			of floors (I’ve seen no engineering info although Mike indicated that 			it has been done). I gave ok insulate exterior walls and asked to be 			called back when remaining rough-in is complete. Later called 			Doug to ask, in case they were not already planning, that at least 			r21 fiberglass be used in exterior walls.

05-07-19	Went to site with Brad and Doug. Discussed new permit for garage 			and then did a walk through. Getting close to being completed. 			Question about heating/air handler/vent. Doug will get information 			from ARC.

Time 03.

EMAIL 05-08-19 From Doug Plummer

Here is the information from ARC.  As I understand it the “stale air” (from the bathrooms) goes into a duct that takes that directly to the outside.  Something in the Minotair System sends it out and doesn’t let it enter back into the supply to the house.  He is installing the system the same way it’s shown on page 18 of this manual.  If you have any further questions you can let me know and I’ll try to get answers for you.

07-30-19	I did the final inspection and will issue a Completion Certificate. The 		outside units for the heat pumps cannot be installed yet do the 			attached garage work. Inside all units installed, will inspect when 			they are installed when inspecting garage.

Time 0.3

David H Lersch

Plainfield Building Inspector