Kenneth DiPaula andAndrea Stern

44 West 77th Street

NY 10024

917-699-1437

Permit # 2018-30

Map/Lot 104/17

renovate apartment

42B Camp Road

08-29-18	Permit 2018-30, 42B Camp Road. Inspected the plumbing in the floor where they cut out the concrete floor to move plumbing due to relocation of bathroom fixtures. Discussed renovations as the whole interior was gutted. Loft will have stairs, not for sleeping, 28-30 inch width and may be 8 inch rise instead of 7-3/4 code. Ceiling is cathedral and the loft height will be short of 7 feet. Just a small loft for sitting.

Time 0.7

09-18-18	Permit  2018-30, 42B Camp Road. Inspected the radiant floor heating pipes and manifold that was pressurized. Gave okay to pour concrete floor.

Time 0.7

11-29-18	Permit 2018-30, 42B Camp Road – inspection of “apartment” area 				electrical/plumbing rough-in prior to completion of insulation and wall 			covering. (Interior partitions etc, still to be installed) Met Todd Godfrey & 		electrician on-site. Reviewed electrical layout. Everything in exterior walls 		complete (rough-in). Neat & clean. Some plate penetrations to be foamed 			(3-4). Todd indicated that spray insulation subcontractor summarily 			caulks/foams all penetrations as part of their scope of work. Discussed 			pending framing, boiler & water heater set-up, future metal-bestos 				chimney for planned woodstove, smoke/co detection, etc.

BRAD

09-08-19	Renewal letter sent in May 2019, no response as of this date. Permit expired 			without a final inspection.

05-27-20	Todd called 443-1004 and said they were finished and needed the final inspection done. I told him the permit expired last year and I never received any response from owner. They are not in town now. I told him I would do the inspection tomorrow.

Time 0.2

05-28-20	I completed the final inspection of the apartment with cathedral ceiling that contains one room with a living space, kitchen and a small loft that due to ceiling height of three feet or more does not meet code for square foot requirement for living space. Also windows too small for egress so it can't be used for sleeping space. A open bathroom that is the mechanical room with propane wall mounted boiler that serves for the radiant heat as well as hot water, contains a sink open, shower (no enclosure), and a toilet and has a door to living area.  I will issue a certificate of completion.

Time 0.9

David H Lersch

Plainfield Building Inspector

Completion Certificate

TOWN OF PLAINFIELD, NH

This certifies that the work described by Building Permit # 2018-30 , at 42B Camp Road, Meriden, NH, Map/Lot 104-17 has been completed in accordance with the provisions of the International Residential 2009 Code and the Codes of the Town of Plainfield.

Description of Work: Renovate 24'x28' apartment with a bathroom, kitchen and living area and a loft (does not meet square footage code for living space). A 12'x24' garage was renovated also.

Portion of structure inspected: Completed renovation.

Applicants Name: Kenneth DiPaula and Andrea Stern

44 West 77th

New York, NY 10024

____________________________May 28, 2020

Building Code Official Signature   Date

David H. Lersch