Walter Janes

1106 Route 12A

667-5040

Permit # 2019-26

Map/Lot 107/01

8'x60' lean to on barn

05-13-19	Inspected lean to on south side of barn. Built as per drawing. Posts set on blocks down three to four feet. He tied the rafters into the barn rafters for additional support as he didn't like the looks of the beam. I suggested he install hurricane clips on rafter to beam on end of lean to. I will issue a Certificate of Completion.

David H Lersch

Plainfield Building Inspector