11-12-19	Rob called to have me see what he was doing in the basement to finish it.

He installed blue foam on walls and built a 2x3 frame with studs, upper and lower plates. He is going to install receptacles and wiring then add more blue foam insulation and finish with fire code class A rating panels.

Time 0.7

11-15-19	I inspected the rough in electrical and looked okay. He is dropping wire down from junction boxes and running along the top of the plate. The ceiling will be a drop ceiling.

Time 0.5

03-31-20	Robert has been sending pictures for each section as he completes the electrical rough in and then when the wall is insulated. Each section is done in the same way, and after I give the okay he covers the wall. He has to move things in the basement as he works that is why I have him send pictures instead of an on site visit each time.

04-21-20	I completed the final inspection of the finishing of the basement by installing studs insulated with blue foam, providing receptacles at required spacing, and covering with sheeting that meets flame spread index. He installed a drop ceiling that is only 6'6" instead of the 7' requirement as the height to the bottom of the joists is 7' in areas where heating ducts or beams are not. Vinyl flooring installed. I will issue a Certificate of Completion.

Time 0.2

David H Lersch

Plainfield Building Inspector

Completion Certificate

TOWN OF PLAINFIELD, NH

This certifies that the work described by Building Permit # 2019-80, at 31 Westgate Road, Plainfield, NH, Map/Lot 108-07 has been completed in accordance with the provisions of the International Residential 2015 Code and the Codes of the Town of Plainfield.

Description of Work: Frame, insulate, provide additional electrical circuits, install drop ceiling and plank flooring, to finish basement for exercise, game room, storage, three areas 14'x25', 12'x20', 12'x15'.

Portion of structure inspected: Finished areas in basement (ceiling height varies due to duct work, beam and is less than seven feet, average 6'6").

Applicants Name: Robert Gattie

31 Westgate Road

Plainfield, NH 03781

April 21,2020

Building Code Official Signature   Date										        David H. Lersch